## Slide 1
EP 01
// network panache
PACKET ANALYSIS DEEP DIVE
Capturing & dissecting live traffic with Wireshark and tcpdump
Lavoisier Cornerstone · lavoisier.dev
network panache // blog.lavoisier.dev

## Slide 2
01
01
OVERVIEW & OBJECTIVES
What we're building, what you'll learn, and why it matters for your career.
network panache // blog.lavoisier.dev

## Slide 3
01
WHAT IS PROMISCUOUS MODE?
By default, a NIC only accepts frames addressed to its own MAC address.
Promiscuous mode tells the NIC to accept ALL frames on the wire — regardless of destination.
This is how a sniffer sees traffic it wasn't meant to receive.
ℹ
CCNA EXAM NOTE Without a SPAN port on a managed switch, your sniffer only sees broadcast traffic and frames addressed to it. Configure SPAN to mirror a port's traffic to your capture interface.
network panache // blog.lavoisier.dev

## Slide 4
02
CAPTURING LIVE TRAFFIC WITH TCPDUMP
BASH
# Enable promiscuous mode
ip link set eth0 promisc on
# Capture HTTP + Telnet to file
tcpdump -i eth0 -w capture_lab01.pcap \
-n -v 'tcp port 80 or tcp port 23'
# Live ASCII output — spot cleartext creds instantly
tcpdump -i eth0 -tttt -A 'host 192.168.1.1'
ℹ The -A flag prints packet payload in ASCII. Cleartext protocols expose credentials immediately.
network panache // blog.lavoisier.dev

## Slide 5
03
PROTOCOL SECURITY COMPARISON
PROTOCOL | PORT | ENCRYPTED? | REPLACE WITH
Telnet | 23 | ✕ No | SSH (port 22)
FTP | 21 | ✕ No | SFTP (port 22)
HTTP | 80 | ✕ No | HTTPS (port 443)
SSH | 22 | ✓ Yes | —
HTTPS | 443 | ✓ Yes | —
network panache // blog.lavoisier.dev

## Slide 6
// key takeaways
WHAT TO REMEMBER
1
Promiscuous mode: NIC accepts ALL frames, not just those addressed to its MAC
2
SPAN port required on managed switches — without it you only see broadcast traffic
3
Telnet & FTP transmit credentials in plaintext — always visible to a sniffer
4
Follow TCP Stream in Wireshark reconstructs full client-server conversation
network panache // blog.lavoisier.dev

## Slide 7
THAT'S A WRAP
Packet Analysis Deep Dive — EP 01
-> blog.lavoisier.dev
-> commandcenter.lavoisier.dev
-> lavoisier.dev
network panache // blog.lavoisier.dev